## Slide 1
Portable Ladder Safety
Training
©2014 PROFESSIONAL RESOURCES IN SYSTEM MANAGEMENT, LLC | PROPRIETARY & CONFIDENTIAL

## Slide 2: Training
  To be completed by new employees and on an annual basis.
  Training is 2 parts:
    Ladder Safety: https://www.youtube.com/watch?v=THGCVTxgY7g
      Safe Ladder Use
      Set-up procedures and components of a ladder
      Hazards associated with ladders
    2. Review these slides after watching the video.

## Slide 3: Ladder Safety
In the United States, one person almost every day of the year is killed by
falling from a ladder; approximately 300 deaths and 130,000 serious injuries.
Probably hadn’t thought much about it, huh? After all, ladders are one of
those tools we use every day and take for granted. Yet, if a falling accident
occurs from a ladder, the chances are excellent the accident will result in
injury or death.
Besides the expense of Worker’s Compensation Claims, the really
important issue is the pain and suffering a fall injury may bring - to you as a
victim, or to your survivors - and the lost productive time to your employer.
Fortunately, almost all falls are preventable – if the fundamentals of ladder
construction, use and safety are understood.

## Slide 4: Ladder Safety
For all their apparent simplicity, two primary hazards are associated with the
use of ladders. The hazards are…
  Falls (and the sudden stop at the bottom!)
  Electrical hazards
    Electrocution
    Shocks (often with resulting falls with sudden stops at the bottom!)
In this course, you will learn how ladders are designed and constructed,
how to use portable ladders safety. You will also learn about the safety
equipment necessary to safely climb fixed ladders at industrial facilities.
As in any knowledge-based course, the development of hands-on skills in
the deployment, use and maintenance of fall arrest equipment is essential
before climbing industrial fixed ladders.

## Slide 5: Ladder Safety
Portable ladders and electricity
Right up front, the student should understand that portable ladders (of any type) and electricity truly do not mix!
Portable ladders are difficult to handle and can easily an accidentally break lighting and other power fixtures.
Worse, portable ladders used outdoors can contact elevated high tension supply lines by accident resulting in electrocution. In many cases, conductive ladders do not have to contact the line – they can merely come sufficiently close to it to cause a short circuit through the ladder to ground.
Do not use metal (or wet) ladders when working near power-lines or fixtures. Keep all ladders at least ten feet away from residential power-lines and much further away from larger power-lines.

## Slide 6: Ladder Safety
Some safety pointers for using straight and extension ladders
  1. Keep your belt buckle between the rails!
    Keeping your belt buckle between the rails means that you have not
    extended your weight far over one rail causing the ladder to over-
    balance, slip and fall.
  2. Never hand carry loads up a ladder!
    If tools or supplies are required, carry them in your pocket, in a tool
    belt, or lift them from the ground in a line.
  3. Always use a three-point stance!
  One hand and both feet on the ladder; both hands and one foot on the ladder. If you must work with both hands, hook one leg over a rung to hold and support you.

## Slide 7: Ladder Safety
  4. Never stand on the ladder’s top three rungs!
  Its easy to overbalance and fall off.
  5. Never use a ladder that is damaged or weakened!
  6. Never “walk” a ladder into position while you are on it!
    Climb down and re-position the ladder from the ground.
  7. Use care around electrical fixtures!
    You can get an electrical shock on any ladder, but dry fiberglass
    and wood ladders do not normally conduct electricity. Using
    aluminum ladders around electrical fixtures can result in
    electrocution.

## Slide 8: Ladder Safety
  8. Never use a ladder in front of a door unless it is locked, blocked or guarded!
  9. Never use a ladder in a strong wind!
  10. Never have more than one person on a ladder at one time!
  11. Never carry a ladder in the vertical position.
  Carry a ladder in the horizontal only.
  12. Never jump from a ladder!
  13. Be certain you are in good enough physical condition to climb!
    Includes not being under the influence of alcohol or drugs that
    make you dizzy, drowsy or subject you to fainting.

## Slide 9: Ladder Safety
  14. Make sure ladders are kept free of oils, greases or other contaminants that may cause slipping!
  15. Use ladders only for their intended purpose!
    Ladders are not bridges. If you need to bridge a gap with a ladder, a
    whole different load bearing analysis must be done to ensure
    safety.
  16. Secure ladders subject to displacement by other inadvertent workplace activities!
  17. Keep areas around tops and bottoms or ladders clear!
  18. Do not move shift or extend ladders while in use!

## Slide 10: Ladder Safety
Portable ladders are normally one of three types…
    Straight
    Extension
    Step-ladders
Portable ladders are normally constructed on one of three materials…
    Wood
    Aluminum
    Fiberglass
Wood ladders are difficult to maintain and have a limited service life. They are used less than they used to be.
Aluminum ladders are light-weight, maintenance-free, strong for their weight and bend before they break. Aluminum ladders are good general service ladders unless exposure to heat or electricity is expected.
Fiberglass ladders are strong, durable and relatively stable to heat and electricity. They are good general service ladders but are somewhat heavy.

## Slide 11: Ladder Safety Review

## Slide 12
is awarded to:
Portable Ladder Safety Training
Certificate of Completion
Computer Based and Instructor Lead
Date:
Name of Instructor

## Slide 13
THANK YOU
UNEQUALLED EXPERIENCE, INVALUABLE RESULTS.
©2014 PROFESSIONAL RESOURCES IN SYSTEM MANAGEMENT, LLC | PROPRIETARY & CONFIDENTIAL