## Slide 1
Hearing Conservation / Noise Exposure
SAFETY TRAINING
©2014 PROFESSIONAL RESOURCES IN SYSTEM MANAGEMENT, LLC | PROPRIETARY & CONFIDENTIAL

## Slide 2: OSHA Requirements
OSHA 29 CFR 1910.95
  The employer shall administer a continuing & effective hearing conservation program for employees exposed to 85 dB or more on an average 8 hr/day.
  Monitor by instruments
  Audiometric Testing
  Training must be initial and annual!
BOTTOM LINE
If you are exposing yourself to hazardous noise levels unprotected…it’s not a matter of whether you will develop hearing loss but when you will develop hearing loss…the odds are VERY RARELY beaten.
Notes: Hearing loss #1 disability & cost to tax payers
  2. Must have hearing conservation training on an annual basis
3. Affects of noise: a. Difficulty understanding conversation, particularly in background noise…high frequency hearing loss affects ability to hear consonants. Quality of environmental sound is diminished. b. ”Ringing in Ears” – tinnitus
4. Types of Protection: earplugs (pre-formed & hand-formed), noise muffs, helmets
5. Why we do audiograms- Important to receive feedback before it becomes a problem….not five years down the road when it definitely is a problem

## Slide 3: Training
  To be completed by new employees and on a annual basis.
  Training is 2 parts:
    Hearing Conservation Safety Training Video : https://www.youtube.com/watch?v=90t0_LuOHbk
      Effects of loud noise on the ears
      Types of hearing protection
      Hazards associated with noise
    2. On the job training from a supervisor or manager
      Complete as necessary

## Slide 4
PARTS OF THE EAR
Outer Ear
Middle Ear
Inner Ear

## Slide 5
Auditory
Nerve
Otolith Organs
Eustachian Tube
Opening to Throat
Ossicles
Middle Ear
Ear Drum
External Ear
Cochlea

## Slide 6
TYPES OF HEARING LOSS
Conductive: Problem with outer or
middle ear system.
Sensorineural: Loss located in the
inner ear system.
Mixed: Combination of conductive and
sensorineural hearing loss.

## Slide 7
CAUSES OF SENSORINEURAL
HEARING LOSS
High Fever
Medications
Infections
Pathology
Childhood Illness
Presbycusis (age)
Congenital
Noise Exposure

## Slide 8: Decibel (dB) Levels
0 dB - Threshold of hearing
65 dB - Average human conversation
85 dB - Damage-risk noise limit
120 dB - Threshold for discomfort
140 dB - Threshold of pain
160 dB - Ear drum rupture

## Slide 9
TYPES OF NOISE
Weapons Firing (140+ dB)
Factory Work (85 dB)
Aircraft (90-120 dB)
  CH-47D - 112dB
  UH-60A – 108dB
Lawn Mowers (95-100 dB)
Motorcycles (110 dB)
Speed Boats (100 dB)

## Slide 10
NOISE INDUCED HEARING LOSS
Temporary Threshold Shift (TTS):
Single exposure to noise, hearing recovers
within a few minutes to hours.
Symptoms: Fullness, tinnitus (ringing)
Permanent Threshold Shift (PTS):
No/partial recovery. Hearing loss remains.
Treatment: Hearing Aids

## Slide 11
CHARACTERISTICS OF NOISE
INDUCED HEARING LOSS
Painless
Progressive
Permanent
PREVENTABLE

## Slide 12
RULE OF THUMB
If you have to SHOUT, it’s
too LOUD!

## Slide 13
COMPONENTS OF THE HEARING CONSERVATION POGRAM
Noise Hazard Identification
Engineering Controls
Hearing Protection
Monitoring Audiometry
Annual Health Education
Enforcement
Program Evaluation

## Slide 14
NOISE HAZARD IDENTIFICATION
Noise surveys and site visits conducted
by industrial hygiene.
When noise levels exceed OSHA
standards, noise signs/decals must be
posted in area (unit commander or
supervisor responsibility).

## Slide 15
ENGINEERING CONTROLS
Lubrication
Control Vibration
Increase Damping
Use of Mufflers
Enclosing Machines
Use Baffles
Isolate the Operator
Proper Maintenance

## Slide 16
HEARING PROTECTION TYPES
Ear plugs (hand formed, pre-formed, silicon or custom)
Ear canal caps
Noise muffs
Helmets (HGU-56P or other approved aviation helmet)

## Slide 17
RESPONSIBILITY
ALL personnel working in noise hazardous areas must have hearing protection with them at all times.
Hearing protection is issued at no charge to all personnel.
Unit hearing conservation manager MUST maintain an adequate supply of hearing protection.
INDIVIDUAL responsibility to wear hearing protection.

## Slide 18
is awarded to
Hearing Conservation / Noise Exposure
Safety Training
Certificate of Completion
Computer Based and Instructor Lead
Date:
Name of Trainer

## Slide 19
THANK YOU
UNEQUALLED EXPERIENCE, INVALUABLE RESULTS.
©2014 PROFESSIONAL RESOURCES IN SYSTEM MANAGEMENT, LLC | PROPRIETARY & CONFIDENTIAL