## Slide 1
Hydrogen Sulfide (H2S) Awareness
Training
©2014 PROFESSIONAL RESOURCES IN SYSTEM MANAGEMENT, LLC | PROPRIETARY & CONFIDENTIAL

## Slide 2: H2S (Hydrogen Sulfide)
What is Hydrogen Sulfide?
          Colorless gas
          Flammable
          Heavier than air
          Extremely toxic
          “Rotten egg” smell
          Deadens sense of smell
  Health Effects:
  Low concentrations (<10ppm)– irritation of eyes, nose, throat and respiratory system
  Moderate concentrations (10<x>30ppm)– headache, dizziness, nausea, coughing, vomiting and difficulty breathing
  High concentrations (>30ppm)– shock, convulsions, coma, death

## Slide 3: H2S (Hydrogen Sulfide)
Exposure Limits:
  ACGIH TLV (8hr)= 10 ppm
  OSHA ceiling (15 min)= 20 ppm
  OSHA peak (instantaneous) = 50 ppm
  IDLH = 100 ppm
  ATSDR MRL = 0.07 ppm (acute), 0.03 ppm (intermediate)
  Location Classifications:
No Hazard Area
Condition 1 Area – low hazard <10 ppm
Condition 2 Area – medium hazard >10ppm, <30 ppm
Condition 3 Area – high hazard >30 ppm

## Slide 4: Training
  To be completed by new employees and on an annual basis.
  Training:
    H2S Safety awareness training: https://www.youtube.com/watch?v=Hgu1bMyHRqw
      What is H2S?
      Controls and PPE
      Avoiding Exposure
      How to evacuate from a contaminated H2S environment
  Additional H2S Safety Training Video:
    https://www.youtube.com/watch?v=kRjsBJA0OuI (Optional)

## Slide 5: Procedures
  If a H2S alarm was activated at a platform prior to arrival, the pilot should not land at the platform.
  If a H2S alarm becomes activated while on a platform with the aircraft running, the aircraft should immediately depart the platform as safety permits.
  In a situation where the aircraft were shut down on the platform and an alarm is activated, the pilot and crew needs to comply with platform H2S procedures.

## Slide 6
is awarded to:
Hydrogen Sulfide (H2S)
Awareness Safety Training
Certificate of Completion
Computer Based and Instructor Lead
Date:
Name of Instructor

## Slide 7
THANK YOU
UNEQUALLED EXPERIENCE, INVALUABLE RESULTS.
©2014 PROFESSIONAL RESOURCES IN SYSTEM MANAGEMENT, LLC | PROPRIETARY & CONFIDENTIAL